Explanation of Remote Functions

- Button: A button turns on the balance mode if you’re not on the unit. Or If you want the unit to balance on a flat surface by itself.  You do not have to Click A to get on the unit, you can simply turn on the main switch and step on and the unit will automatically turn on the balance mode. Clicking A again will enter pulling mode if need to pull the unit over a curb etc. To exit pulling mode just click A again and the unit will return to balance mode. Note: if you are trying to get on the unit with the unit in balancing mode (example clicking A before you get on the unit) the unit will be leaning backward, this is normal. Just place one foot on the machine while holding the handle bar and the unit will start to level out so you can step up with the other foot.

- Button: B button is for locking scooter with alarm. Turn on main switch and click the B button. If someone tries to get on the unit or move it, the buzzer will ring. To cancel this just press the A button.

- Button: C button changes the mode, click the c button and the unit will beep. 1 beep is beginner mode which limits the speed to 8kmph and slows turning. 2 beeps are the normal mode with full speed of 18km/h and sensitive steering.

- Button: D button just turns the lights off and on.

C@D Buttons together: Recalibrating Gyros.

This is for recalibrating the Gyros and should only be used if you are having issues with the unit balancing. Recalibration of the machines flat and level can be performed by holding down the C and D buttons together and then Turning on the Main switch on the unit. You will have to hold the two buttons down for 10 seconds, you will hear a set of beeps from the unit during this process. You will have to make sure the unit is on a flat surface and the Foot Pedals are parallel to the surface. After the 10 seconds let go of the C and D button and now the unit will be recalibrated to the level you had set the foot pedals too.